Geophysics 224

# Lab. 4 – Seismic refraction with multiple horizontal layers

Introduction

The seismic refraction technique is based on the study of P-wave arrival times, as a function of distance, along the surface of the earth. The first arrival of seismic energy at a detector can be either the direct wave or the head wave (refraction). From observations of first arrival times at various source-receiver distances (offsets) one can determine the speed at which seismic waves propagate through the layers and the thicknesses of the layers.

Let’s assume a model consisting of two layers overlying a halfspace with velocity increasing with the depth (i.e. v3 > v2 > v1).

At short offsets, we will observe the direct arrival. This arrival propagates horizontally along the Earth’s surface at a speed equal to that of the top layer (v1).

At intermediate-to-large offsets, we will observe the head wave from one of the interfaces as a first arrival. This arrival propagates horizontally along the interface at a velocity equal to that of the layer below of the interface.

A traveltime-distance plot would consist of a number of separate refractions in which case several straight line segments are fit to the data to determine the velocities of progressively deeper layers.

## Exercise 1

- From the data provided in the Excel file

Lab4_224_2005_refraction_horizontal.xls,

plot the traveltime curves (time versus distance).

- Draw the best-fit line segments (4) on your traveltime curve.

- Measure the slopes and time-intercepts of the straight line segments on the resulting graph.

- The slope is the inverse velocity (slowness). Thus, from the slopes of the line segments describing the traveltime curve compute the velocity for every layer.

- To calculate the layer thicknesses, Snell’s Law is used to determine the angles that the seismic rays make with respect to each layer. For two layers, Snell’s Law yields:

where θ12 is the angle within the first layer for the two layer case.

The first layer thickness z1 can be obtained from the corresponding time intercept:

For three layers, z2 can be found from:

and

Using the formulas from above, compute the thickness for both layers (z1 and z2).

- Sketch the subsurface structure determined by your graphs and analysis. Label your sketch with the appropriate velocities and thicknesses.

Exercise 2

On the figure of the real data provided, draw the traveltime curves.

From the slope find the velocities, and calculate the thickness of the first layer

March 2006