A1. Magnetotelluric response of a layered Earth

A1.1 Impedance of layer over a halfspace

See Geophysics 424 notes

A1.2 Recursion relation for impedance of multi-layer Earth

Consider a stack of N layers, underlain by a halfspace with conductivity σN

In the nth layer the conductivity is σn and the upper and lower interfaces are at a depth of zn-1 and zn respectively. Let the electric field in the nth layer be defined as the sum of upward and downward propagating signals as :

(1)

The signal has an angular frequency ω and diffuses in the Earth with the propagation constant is defined as

The orthogonal magnetic field can be computed from Maxwell’s equations as

(2)

(3)

Now define the transfer function in the nth layer as:

(4)

At the top of the layer at z = zn-1

(5)

This can be rearranged to give

(6)

Equation (6) can also be written for the base of the layer at z = zn

(7)

Equating (6) and (7) gives

(8)

Now rearrange to get on the left hand side.

(9)

The thickness of the layer is Δzn = zn-zn-1 so we can write

(10)

Expanding (10) gives:

(11)

Rearranging (11) gives:

(12)

Which can be simplified as:

(13)

Now note that the hyperbolic tangent,				(14)

Thus if we divide top and bottom of (13) by then we get

(15)

Can further simplify this as

(16)

Since both Ex and Hy are continuous at an interface, then C must also be continuous across an interface so that

At the base of the stack (z = zn) , we can define and at this interface

This is Wait’s recursion relationship (reference?). Starting from this value, the recursion relation can be used to derive a value for which is the value at the surface of the Earth at z = 0.

(17)

(18)

A1.3 Alternative approach using electric and magnetic fields

Define the electric and magnetic fields in the nth layer as:

(19)

(20)

Now at the base of layer (z = zn) the electric and magnetic fields have values and where the L denotes “lower”.

(21)

(22)

Re-arranging (22) gives

(23)

Adding (21) and (23) gives

(24)

Which can be rearranged as

(25)

Subtracting (21) and (23) gives

(26)

We can now evaluate the Ex and Hy at the top of the layer (z = zn-1) with U denoting “upper”.

where Δzn = zn-zn-1 is the thickness of the  layer

Similarly it can shown that

To evaluate the fields at the surface (z = 0) we can start recursion in the lowest layer.

Here and we can arbitrarily set An=1 giving

Values at the lowest interface can thus be chosen as are thus and

MATLAB  :  MT1D_fields_2009.m

Note:

- Many layers are defined in the model, with the same resistivity for many layers. This is simply a way to force the algorithm to output and at many points.

- Surface MT response is computed and was verified against MT1D_Ex1.m

- Note that is continuous across boundaries.

- Also is continuous since is continuous.

- Dashed lines show how the electric field would decay with depth for a half-space with resistivity value of upper most and lower most layers.

- Can consider that MT measures the impedance of the Earth by measuring the slope of  at z=0. This is because the impedance is proportional to .  When the resistivity of a layer is low, the more rapid decay of electric field with depth decreases at z = 0. This is because  and  are continuous functions with z.

- Note also that the length scale with which varies increases with skin depth.

A1.4 Electric fields within a two-layer Earth

- Frequency = 2 Hz

  - Ex(z) decays at rate associated with skin depth for 1 Ωm

  - At this frequency, a surface measurement of  contains no information about the lower layer

(2) Frequency = 0.8 Hz

- Can now see Ex(z) decaying slowly with z in lower layer, and rapidly in upper layer.

- Note that is continuous at the interface at z = 1 km

- The change in gradient occurs over a finite distance that is related to skin depth.

- At the frequency shown above, this distance is greater than the layer thickness (1 km) so at z = 0 is greater than for the 1 Ωm layer.  This causes ρa to be lower than 1 Ωm

- Note that as frequency decreases, the slope of the dashed lines also decreases. This is because the skin depth increases with decreasing frequency.

(3) Frequency = 0.1 Hz

- Now   at z = 0 is intermediate between the values expected for 1 Ωm and 1000 Ωm

- At this frequency both layers are reflected in the apparent resistivity

(4) Frequency = 0.00001 Hz

- At the lowest frequency has the value for the lower layer (1000 Ωm)

- Note the vertical scale has changed in the plot of Ex(z)

A1.5 Examples of 1-D sounding curves

These examples are also used in GEOP424

Example 1

Example 2

Example 3

Example 4

A1.6 Early example of 1-D magnetotellurics from Meanook, Alberta

- Niblett and Sayn-Wittgenstein (1960) used the Meanook magnetic observatory and long telluric lines to compute one of the first MT responses.

- Figure below shows comparison with a Lithoprobe LIMS site collected during the Alberta Basement transect in the 1990’s

- Units are converted in niblett_1960_at318.m

- Electric fields were also measured electric fields at Meanook by Randy Mackie from 1997 to 2004 using rented telephone lines. I paid the phone bill for a few years and the results were presented in a Physics 499 project by Alex Walcott.

A1.7 Finite difference calculations in 1-D

- Can also solve for electric fields using finite difference approximations

- Not needed, since the 1-D problem can be solved analytically but provides a useful  introduction for 2-D finite difference code.

- At top node (z=0) the electric field is forced  to have value  Ex = cmplx (1,0)

- At the bottom node of the grid, the electric field is set to zero

- Since the electric field is fixed at z = 0, the accuracy of the calculation depends completely on the value of Hy at z = 0

- The finite difference grid is defined by 2 parameters

The first grid spacing is dzstart and increases geometrically.

The grid extends to a maximum depth of zmax

A1.7.1 Computing Hy at surface (z=0)

- Simplistic first order approximation is not very accurate. If the first two nodes are defined as [z1, zz] and the electric fields at these nodes are [E1, E2]

Note that  and

- A cubic approximation using the first 3 nodes is significantly better, as shown below. If the first three nodes are defined as [0, zz, z3] and the electric fields at these nodes are [1, E2, E3] then can look for an interpolated function as

Which can be differentiated to give

At z = 0

assuming

A1.7.2 Effect of overall meshsize for 100 Ωm halfspace

Code : MT1D_FD_halfspace_meshsize_v2.m

- Can see that the depth extent of the FD grid (zmax) needs to be 2-3 times greater than the skin depth at a given frequency.

- This example uses cubic interpolation to compute Hy at z = 0

- Obviously the value of zmax used will be determined by the lowest frequency (longest period)

A1.7.3 Effect of mesh texture for 100 Ωm halfspace

- To select the size of the first row (dzstart) need to consider the skin depth at the highest frequency which is 1000 Hz (shortest period).

- In first figure δ (f =1000 Hz) = dzstart and the apparent resistivity and phase at the highest frequency are unacceptably large. Cubic calculation for Hy is much better than the linear calculation.

- Below shows the δ (f =1 000 Hz) = 3 dzstart  and the cubic Hy calculation is now accurate at f = 1000 Hz to around 1%. The linear Hy calculation is very inaccurate.

- Below shows the δ = 10 dzstart  and the cubic Hy calculation is now accurate at f = 1000 Hz. However the linear Hy calculation is still inaccurate.

- Figure below shows the error in apparent resistivity and phase in pseudosection format.

A1.7.4 Effect of mesh texture for 3 layer Earth

References

Niblett, E. R., and C. Sayn-Wittgenstein, Variation of Electrical Conductivity with Depth by the Magneto-Telluric Method, Geophysics, 25, 998-1008, 1960.