University of Alberta Telephone Instructions for M9009 sets

#### Call Forward

This allows you to program your telephone to reroute calls to another telephone number.

- Lift the handset and listen for dial tone.

- Dial *72 if you get a dial tone again, enter the number that you want to forward to.

- Hang up.

When you are ready to receive calls at your telephone again,

- Lift the handset and listen for dial tone.

- Dial *73 if you hear complete silence, it indicates that you have cleared the call forwarding. Hang up.

You may want to test that your call forwarding is turned off by asking someone to call you.

#### Call Transfer

This feature provides both announced and unannounced Call Transfer calls within the University system.

To transfer a call:

- Flash switch hook or press link button.

- Listen for 3 beeps and dial tone (caller is on hold).

- Dial the number you want to transfer the call to; wait for ringing.

- The transfer can be completed by hanging up after you hear ringing on the other end or you can stay on the line to announce the call.

- The call transfer is completed when you hang up.

If you get a busy signal or a ring no answer, flash the switch hook or press the link button to return to the caller.

#### Conference (three-way)

This feature allows you to establish a conference call between yourself and two other parties.

- While on a call, flash the switch hook or press the Link button.

- Listen for 3 beeps and dial tone.

- Dial the number that you want to conference with and wait for the person to answer.

- Flash the switch hook or Link button (first caller is on hold), dial the number of the next person you want to conference with; wait for the person to answer.

- Flash the switch hook again; all three callers are now connected.

If you get a busy signal or a ring no-answer, flash the switch hook or press the Link button to return to the caller.

#### Call Pick Up

Your telephone may be assigned to a call pick-up group. If you are in the same call pick-up group as a phone that is ringing, you may answer the call from your own set.

To pick up a call:

1. Lift handset and listen for dial tone.

2. Dial 623 and the call will be brought over to your telephone.

#### Ring Again

If after dialing a DN you receive a busy signal, you may activate the Ring Again feature. The system will notify you when the line becomes free and redial the number for you automatically.

- You have dialed a DN and received a busy signal.

- Flash the switch hook or press the Link button and listen for 3 beeps and dial tone.

- Dial 621 and hang up.

You are notified by short bursts of ring when busy number comes free. Lift the handset and the system will automatically dial the number.

If you wish to cancel Ring Again before you have been notified that busy phone is free, lift handset and listen for dial tone. Dial 302 and hang up.

#### Last Number Redial

This feature allows you to redial the number last called.

Lift the handset and listen for dial tone. Press the Redial key (if available) or  Dial 6289; the last number that you had dialed will be redialed automatically.

Remembering the last incoming call

  - without lifting the receiver, you can view the telephone number of the last incoming call by pressing  * .  (You must have caller ID for this to work.)

### M9009 Option button

Under sliding panel located below the display

Set 5 options by pressing the key to see the choices

- Change the language

- Choice of English or French

- set the time and date

- set the ringer tone and ringer volume

- Choose one of four different ring tones.

- Adjust the ringer volume by pressing the volume bar located below the dial pad

- Use the save button to end when you are satisfied with the ring tone and volume

- Turn the light off

- Used with a memory key to light when you have a feature turned on,  eg. lights up when Call forwarding  is activated

- enter your  area code (780)

- if you want local calls to appear without the area code.

To change any of the five options:

- Don’t pick up the receiver

- slide the panel and press the “set options” key

- press  *  to move through the list of options one at a time

- press the selected number again and follow the instructions on the display to change the option.

#### Saving numbers in  6 memory keys

- press “save” and follow the instructions on the display

- press the memory key where you want to save the number

- use the dial pad to enter the number (press 9 and number for off- campus calls)

- press “save”

To erase the memory key

- press the memory key, to see contents

- press  #  twice to erase

# QUESTIONS AND PROBLEMS

No dial tone

- Check the phone cord is attached properly at the wall and under the phone.

No information appears on the display and volume is low

- Make sure the power adapter (M9009) is plugged into the electrical outlet.

Can’t hear or be heard

- Check the receiver cord is inserted securely into the jack

Still have problems?  Contact AICT Telephone Services 780 492-3422